## Slide 1: AHC OTA – DP170 Firmware updates to Point to Point Alt HAN Devices
Conflict between SLA 8.1.2 and Requirement 159
Date: June 2021

## Slide 2: Wider Smart metering architecture
The Standard HAN setup:
In most cases, a standard smart metering installation will include gas and electricity smart meters an In-Home Display (IHD)
and a Communications Hub (CH).
All smart devices are within the expected propagation distance (2.4GHz and 868MHz) of the Communications Hub for the Standard HAN to be able to connect them.
Smart Metering Implementation Programme:
Energy Suppliers are required to roll out smart metres to all their domestic and small
business customers. The total expected cost of the Smart Metering Implementation Programme is currently estimated at £11 billion.
Key Smart Metering Terminology:
DCC – Data Communication Company
WAN – Wide Area Network
IHD – In-Home Display
CH – Communications Hub
HAN – Home Area Network
SMKI – Smart Metering Key Infrastructure
SEC– Smart Energy Code
2

## Slide 3: Alt HAN Building Use Cases
Alternative HAN is required when one or both of GSME and IHD are out of Zigbee range of the CH and ESME
This could be in a number of Building Types (see graphics) where:
Either of the IHD or GSME might be Remote
Both might be Remote but Close Together
Both might be Remote but Far Apart from each other
The GSME may be Very Remote
In this context:
Remote = out of Zigbee range of the CH and ESME
Close Together = both within Zigbee range of a single mains power outlet in the premise
Far Apart = not within Zigbee range of a single mains power outlet in the premise
Very Remote = out of Zigbee range of the CH, ESME and of all mains power outlets in the premise
Notes: Slide speaks for itself

## Slide 4: AHC Devices
There are 4 different device types known as ‘bridges’ also known as B1, B2, B3 and B4.
These bridges are configured to form 3 different ‘solutions’: Solutions A, B and C.
  Solution A: Uses B1 and B2 when either IHD or GSME are out of range or they both are but close together
  Solution B: Uses B1, B2a and B2b when IHD and GSME are out of range and far apart
  Solution C: Uses B1, B3 and B4 when IHD is out of range and GSME is very remote (does not have nearby mains electricity to power any bridges)
Each bridge joins the ZigBee network as Range Extenders to tunnel traffic. This is achieved via the standard DUIS whitelist functionality and performed by Service Users
AHC bridges support the following Zigbee clusters
What happens when an IHD encounters a normal HAN and an AHC device is connected?
The device uses the network with the least hops.
 | Server side | Client side
B1-3 mandatory clusters | Basic, Key establishment | Key establishment
B1-3 optional clusters | Keep-alive | Keep-alive
B4 mandatory clusters | Basic, Key establishment | Key establishment
B4 optional clusters | Keep-alive | Keep-alive, Time

## Slide 5: Solution Decisions introduction
The implementation of a number of the requirements and solution options could significantly impact the cost and complexity of the solution. Subsequent slides highlight these items for decision by industry.
These are at a high level:
Energy Suppliers shall be able to confirm that Firmware upgrades for Alt HAN Co Devices have been successful – This requires devices to support for sending GBCS alerts and using SMKI credentials
Energy Suppliers shall be able to read the current Firmware version on Alt HAN Co Devices – This requires devices to support for receiving and processing GBCS commands, sending GBCS responses and using SMKI credentials
Energy Suppliers shall be able to replace any SMKI credentials on Alt HAN Co Devices – This requires devices to support for receiving and processing GBCS commands, sending GBCS responses and using SMKI credentials
Alt HAN Co Devices shall continue to join the HAN as CADs – This requires the Comms Hub to support the distribution of firmware to another device type

## Slide 6: Solution Decision 1
Alt HAN Bridges currently operate at the Zigbee network level. They are not type 1 devices and cannot interact with anything outside of the HAN. SECMOD 7, which introduced OTA via the DCC for devices other than ESME/GSME, introduced a post firmware upgrade alert sent by the device to the DSP.
To support this requirement and to align with the SECMOD 7 introduced behaviour, the AHC solution would need to:
Become a SMKI registered user
Install SMKI device and organisation credentials during manufacturing
Support the creation and sending of a GBCS alert
If this requirement is not delivered, Service Users will only be able to infer the successful delivery via the additional instrumentation from the Comms Hub delivered via SECMOD 7.
Given the significant increase in complexity of the AHC bridges, a decision is required from Industry as to whether this is a mandatory requirement.
Requirement | Impact
Energy Suppliers shall be able to confirm that Firmware upgrades for Alt HAN Co Devices have been successful | Complexity in Product and supply chain

## Slide 7: Solution Decision 2
As per decision 1, this requirement drives similar additional complexity via support for GBCS / SMKI message processing
To support this requirement the AHC solution would need to:
Become a SMKI registered user
Install SMKI device and organisation credentials during manufacturing
Support the processing of a GBCS non-critical command and the creation / sending of a GBCS response
If this requirement is not delivered, Service Users will be dependent on the DSP successfully receiving any post firmware upgrade alert and only be able to infer the successful delivery via the additional instrumentation from the Comms Hub delivered via SECMOD 7.
Given the significant increase in complexity of the AHC bridges, a decision is required from Industry as to whether this is a mandatory requirement. N.B. if decision 1 is to include the associated requirement, the incremental impact of this requirement is minimal
Requirement | Impact
Energy Suppliers shall be able to read the current Firmware version on Alt HAN Co Devices | Complexity in Product and supply chain

## Slide 8: Solution Decision 3
As per decision 1, this requirement drives similar additional complexity via support for GBCS / SMKI message processing
To support this requirement and to align with the SECMOD 7 introduced behaviour, the AHC solution would need to:
Become a SMKI registered user
Install SMKI device and organisation credentials during manufacturing
Support the processing of a GBCS critical commands and the creation / sending of GBCS responses
If this requirement is not delivered, there is a risk of device replacement should there be a compromise in any of the ACB, root or recovery credentials.
Given the significant increase in complexity of the AHC bridges, a decision is required from Industry and SSC as to whether this is a mandatory requirement. N.B. if decision 1 is to include the associated requirement, the incremental impact of this requirement is reduced.
Requirement | Impact
Energy Suppliers shall be able to replace any SMKI credentials on Alt HAN Co Devices | Complexity in Product and supply chain

## Slide 9: Solution Decision 4
AHC has included this requirement to drive a discussion on whether this SEC MOD should attempt to reduce the complexity of DCC change with a goal of reducing the overall delivery cost. AHC bridges currently join the HAN via the CCS01 command as a CAD. To continue with this behaviour post OTA is expected to require CH firmware change to support delivery of firmware to CADs (as it is understood that the CH will check the device type prior to delivering firmware).
An alternative is to join the HAN as a PPMID. This is expected to reduce / remove CH firmware development by utilising the SECMOD 7 delivered functionality. This option would require consideration of:
DUIS updates to support DSP differentiation between PPMIDs and AHC bridges that appear as PPMIDs
CH behaviour with non-PPMID devices joining the HAN as PPMIDs – understood that there may be an issue with CSPN CHs in relation to how they treat the Device
CH capacity for all AHC bridges acting as PPMIDs in addition to other HAN devices – understood not to be an issue
This decision requires Industry and TABASC input.
Requirement | Impact
Alt HAN Co Devices shall continue to join the HAN as CADs | Volume of change for DCC

## Slide 10: DCC SECMOD7 process flow
The shaded area highlights the interactions where either:
The HAN Device confirms successful Firmware upgrade
The Service User requests the current Firmware version from the HAN Device
Both interactions require SMKI device and organisation credentials to be present on the HAN Smart Energy Equipment and recorded in the DSP

## Slide 11: Further details
SMKI Registration Authority Policies and Procedures - https://www.smartdcc.co.uk/customer-hub/consultations/smki-registration-authority-policies-and-procedures-rapp/
SECAS SECMOD7 material - https://smartenergycodecompany.co.uk/modifications/Firmware-updates-to-ihds-and-ppmids/
SECAS SECMOD7 modification report - https://smartenergycodecompany.co.uk/download/18695
  Device post upgrade Firmware alerts introduction – proposal (p18) and introduction (p27)
  PPMID CPA certification non-requirement (p16)

## Slide 12: Further details
SECAS SECMOD7 modification report – Alerts sent to Responsible Suppliers
“The first Alert would be sent to all Responsible Suppliers (except for the sender as the sender would receive a Service Response) once the DCC has processed the Service Request to distribute the Image. The Alert would include a list of specific Device IDs that were referenced in the original Service Request.
The second Alert would be generated by the Communications Hub and sent to all Responsible Suppliers with confirmation of success/failure of distribution to the Product. This would confirm one of the following:
  Image Discarded
  Hardware Version Mismatch
  File Transfer Failure
  File Transfer Success
The third Alert will be a Device Alert sent to all Responsible Suppliers confirming the Firmware version on the Device. The discussions around the mechanism for this Alert can be found in section ‘Firmware activation Alert mechanism’ sub-section below."