## Slide 1: MP082 ‘2.4Hz Channel Management’ raised by Angel Oses de Leon of Scottish Power

## Slide 2: Background
Issue
As the Smart Metering rollout progresses, more and more Devices will be installed and will be operating simultaneously on the same 2.4GHz Channel.
Devices will be co-located and competing for access for the available ZigBee radio Channels.
The ZigBee 2.4GHz Channel selected at install will be set for the life of the Smart Metering System unless the system is subject to external intervention. This would be via a site visit involving a Communications Hub exchange and a subsequent re-commissioning of the HAN.
Impact
Suppliers have reported some performance issues noted by customers including
    Other Device losing connectivity
    Interference; and
    Loss of Smart data
    Communications Impact between Devices

## Slide 3: Solution Options
Ref. | Description | Ability to manage 2.4GHz Channels | CH Impact | Meter Impact | IHDs/PPMIDs Impact | Specification changes required | Est. time to deliver
1 | The Communications Hub (CH) performs internal assessment to select the best channel by continuously monitoring the channel. No external triggers from Devices / DCC users / CSP is supported. Number of channels changes per week mandated. Assessment could be based on RSSI / LQI / Retry rate / Failure rate. | Medium Only initiates changes based on Radio Frequency (RFI) environment seen by CH. | Low or High Depends on impact of updated SEP stack on Random Access Memory (RAM) constraints. | Limit number of changes to conserve GSME battery. Notification mechanism of intended channel change requested. |  | GBCS CHTS SMETS | 6 Months Note, longer real-life testing with meters and PPMIDs needed to determine HAN stability.

## Slide 4: Solution Options
Ref. | Description | Ability to manage 2.4GHz Channels | CH Impact | Meter Impact | IHDs/PPMIDs Impact | Specification changes required | Est. time to deliver
2a | The Communications Hub performs channel change by external trigger that can be sent by the Communications Service Provider (CSP) to avoid DUIS changes. Communications Hub does not continually monitor link quality and take any actions of its own. | Low Requires manual intervention. Not driven by Radio Frequency conditions. | Medium to High Additional changes to Device management platform. | Limit number of changes to conserve GSME battery. Notification mechanism of intended channel change requested. |  | GBCS CHTS | 

## Slide 5: Solution Options
Ref. | Description | Ability to manage 2.4GHz Channels | CH Impact | Meter Impact | IHDs/PPMIDs Impact | Specification changes required | Est. time to deliver
2b | The Communications Hub performs channel change by external trigger that can be sent by DCC Users through the DUIS. CH does not continually monitor link quality and does not take any actions of its own. | Low Requires manual intervention. Not driven by local Radio Frequency conditions | Medium to High | Limit number of changes to conserve GSME battery. Notification mechanism of intended channel change requested. |  | GBCS CHTS DUIS | 6 Months

## Slide 6: Solution Options
Ref. | Description | Ability to manage 2.4GHz Channels | CH Impact | Meter Impact | IHDs/PPMIDs Impact | Specification changes required | Est. time to deliver
3 | Implement 2.4GHz Frequency Agility aligned to Sub-GHz Frequency Agility Solution. | High Most complete solution, and mirrors sub-GHz implementation. |  |  |  | GBCS CHTS DUIS SMETS | 

## Slide 7: Solution Options
Ref. | Description | Ability to manage 2.4GHz Channels | CH Impact | Meter Impact | IHDs/PPMIDs Impact | Specification changes required | Est. time to deliver
4 | Use the Trust Centre Swap Out (TCSO) Mechanism which is a GBCS requirement to obtain a Change of Channel. In other words, perform a Virtual TCSO. The process can either be triggered by the CH or via a new Service Request that can also include the new Channel Number if needed. | Low Requires extra code which can be managed and mitigated through the Firmware Upgrade. | Low | No Change | No Change | No Change | Should not be long as the CH has already implemented the TCSO as part of the GBCS requirement. However, it will need to implement a mechanism to trigger the process and to act on the new Service Request if materialised.

## Slide 8: Next steps
Discuss and select Solution Options
Business Requirements