## Slide 1: SEC Change Monthly Working Group Meeting – March 2022

## Slide 2: Competition Act Compliance

## Slide 3: SECMP0010 ‘Introduction of triage arrangements for Communications Hub’ raised by Emma Johnson from British Gas

## Slide 4: Objectives of the Working Group
The business requirements
The proposed solution
NOTE
REVIEW
The issue identified under SECMP0010
NOTE
AGREE
SECMP0010 is ready for Preliminary Assessment
SECMP0010 'Introduction of triage arrangements for Communications Hub'

## Slide 5: Summary
What is the issue?
When installation of a CH is unsuccessful is it sent back to the CSP.
The CSP will then diagnose the CH and verify if it is faulty.
Non-faulty CHs incur a reconditioning fee.
Only a certain percentage of are found to be genuinely faulty.
SECMP0010 'Introduction of triage arrangements for Communications Hub'

## Slide 6: Business requirements
Ref | Requirement
1 | Implement a Supplier Unlock Code that allows the factory reset of a Communications Hub (CH) to be automatically executed by the Device.
2 | A Supplier Unlock Code must be requested from the Communication Service Provider (CSP) via the Data Service Provider (DSP).
3 | After receiving a Supplier Unlock Command, should a Supplier attempt to unlock a CH and the CH not function enough to allow the injection of the command, or deem itself to be faulty thereby rejecting the command, then the CH shall be returned by the Supplier to the DCC as per the existing returns process.
SECMP0010 'Introduction of triage arrangements for Communications Hub'

## Slide 7: Business requirements cont.
Ref | Requirement
4 | DCC to either supply equipment through a catalogue service, or specify the minimum requirements needed for a Supplier to adequately shield a CH themselves.
5 | The CH shall maintain a count of how many times it has been successfully unlocked by a Supplier Unlock Command.
6 | The Supplier Unlock Process and existing DCC Returns Process are to be independent of each other (although the Supplier Unlock Process may precede the DCC Returns Process).
SECMP0010 'Introduction of triage arrangements for Communications Hub'

## Slide 8: Proposed Solution
Implement a Supplier Unlock Code that allows the factory reset of a CH to be automatically executed by the device, upon which it would then return to a locked state.
A factory reset would constitute the clearing of any WAN routing information, all consumer sensitive data on the GPF and removal of all entries in the CHF and GPF Device Logs.
A Supplier Unlock Code must be requested from the CSP via the DSP, have anti-replay protection and be unique to a specific CH.
The Smart Metering Inventory will need to be updated to move a CH from the Decommissioned state to the Pending state to allow the device to be installed.
SECMP0010 'Introduction of triage arrangements for Communications Hub'
Notes: - discuss development of dynamic reporting & consider whether members think this should be tackled as a ‘part B’

## Slide 9: Working Group questions
Is there anything else the business requirements should consider?
Are the business requirements suitable to address the issue?
SECMP0010 'Introduction of triage arrangements for Communications Hub'

## Slide 10: Next steps
Request DCC Preliminary Assessment
SECMP0010 'Introduction of triage arrangements for Communications Hub'

## Slide 11: Any further comments?
Khaleda Hussain

## Slide 12: MP195 ‘Security Sub-Committee guidance on Device Assurance’ raised by Gordon Hextall on behalf of the Security Sub-Committee

## Slide 13: Overview
Background
The security controls in the SEC do not currently support the triage and refurbishment of Devices
Issue
SEC Parties have demonstrated a business need for the CPA Certification process to support Device triage and refurbishment
MAPs and Suppliers are currently holding Devices in warehouses that have not been fully installed, but have no defects
Guidance is not currently referenced in SEC and therefore does not provide SEC Parties with certainty they need
Once installed, or partially installed, and then removed Devices are not able to be re-installed on the DCC network
SSC has developed guidance for Device triage, currently published on the SEC website
MP195 ‘Security Sub-Committee guidance on Device Assurance’

## Slide 14: Objectives of the Working Group
The Refinement Consultation responses
REVIEW
MP195 ‘Security Sub-Committee guidance on Device Assurance’

## Slide 15: Refinement Consultation responses - Solution
Do you agree the solution will resolve the issue?
Do you agree with the proposed implementation?
Do you agree the legal text delivers the solution?
Do you agree the document title should be ‘Device Security Assurance and Triage’?
MP195 ‘Security Sub-Committee guidance on Device Assurance’

## Slide 16: Refinement Consultation responses – Impact assessment
Will there be an impact on your organisation to implement the solution?
How long would your Party need to implement?
Will your organisation incur costs?
MP195 ‘Security Sub-Committee guidance on Device Assurance’

## Slide 17: Refinement Consultation responses – Case for Change
Do you believe this will better facilitate the General SEC Objectives?
What are the impacts or benefits to consumers?
Do you believe the modification should be approved?
MP195 ‘Security Sub-Committee guidance on Device Assurance’

## Slide 18: Next steps
16 Mar – 6 Apr – Modification Report Consultation
20 Apr – Change Board Vote
15 Mar – Change Sub-Committee requested to approve Modification Report
MP195 ‘Security Sub-Committee guidance on Device Assurance’

## Slide 19: Any further comments?
Kev Duddy

## Slide 20: MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’ raised by Terry Jefferson from the Energy and Utilities Alliance (EUA)

## Slide 21: Objectives of the Working Group
The next steps
AGREE
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’
The issue is clear and defined
AGREE

## Slide 22: GSME impacting IRPs
IRP642 - Reclarifying trigger for Alert Code 8F69
IRP644 - CH energy scan if GSME is in PPM with credit out
Changes to GBCS section 10.2.2.2 implemented in GBCS v3.2 aimed to clarify the timing of the Alert 0x8F69 when establishing a tunnel
Devices can behave in different ways when a Sub-GHz GSME in prepayment mode:
runs out of credit whilst the Communications Hub is undertaking an energy scan, and
is not in a non-disablement period
It did not specify this Alert should only be sent for the first establishment of a tunnel
This clarifies that the Device should not receive or execute Commands until it next turns on its HAN radio
This clarification will confirm that a tunnel only needs to be established the first time
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 23: ESME impacting IRPs
IRP634 - Future start date-time on Limit APC [n] Level & ECS47e
IRP639 - Addressing ZCL Report Event Status other than 0x02 or 0xFE
The SMETS does not currently detail the Device requirements when an Auxiliary Proportional Controller (APC) [n] Limit Period / APC [n] Setting Period is in force, and then a Command to set a new such period is received by the Device.
The GBCS details requirements for processing Demand Response/Load Control (DRLC) cluster Report Event Status ZCL commands from HAN Connected Auxiliary Load Control Switches (HCALCS)
This clarification will confirm that no log entry needs to be created on the ESME if any other Command is received
The only commands it refers to are: Event Status 0x02 (Event started); or Event Status 0xFE (Event Rejected)
This clarifies that the Device should immediately end any current period, when a valid Command to set a new period is received.
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 24: Non-Device impacting IRPs
IRP637 - Query cross-ref - GBCS v3.2 table 13.2.4.4
GBCS Table 13.2.4.4 details how Devices construct responses to CS02a Commands. The related requirements are found in section 12.3 and 12.4.
This change will add the correct references to section 12.3 and 12.4.
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 25: CRP630 - Provision for additional HAN data items for APC
Provision for additional HAN data items for APC
GBCS and SMETS sets out the requirements for Devices with an APC either as part of the ESME or a Standalone APC (SAPC).
ESMEs with APC and SAPCs currently share the Auxiliary Controller Calendar over the HAN
Impact
The current drafting of the technical specifications does not include all information that these Devices could share with the Devices on the Home Area Network (HAN).
However the mechanism does not fully detail the entries and is therefore not useful
In addition, the Auxiliary Controller [n] State, Limit or Override applied and the use of the Boost button by the consumer are not shared with the HAN
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 26: Implementation
Implementation Approach
Legal text
Does the Working Group have any comments about the draft legal text included?
Legal text defined by TSIRS as part of the IRP development
November 2022
Dependent on decision by end of June 2022
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 27: Case for Change
SEC Objectives
Proposer believes this better facilitates SEC Objective (a)
Consumer benefits
For CRP630 consumers will benefit from having the additional data items shared over the HAN to connected Devices
Impacts and costs
No DCC costs
Will other SEC Parties incur costs from these changes?
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 28: Questions for the Working Group
Should the modification proceed to Refinement Consultation?
Are these issues affecting SEC Parties?
Do any Device Manufactures have feedback regarding implementation timescales?
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 29: Next steps
3 Mar – Presenting the issues to TABASC
7 Mar-25 Mar – Refinement Consultation
6 Apr – Discuss responses with Working Group
MP193 ‘Incorporation of Category 3 Issue Resolution Proposals into the SEC – Batch 6’

## Slide 30: Any further comments?
Kev Duddy

## Slide 31: MP181 ‘Meter Asset Provider access to asset related data held by the DCC’ raised by Lynne Hargrave of Calvin Capital

## Slide 32: Objectives of the Working Group
The Proposed Solution
The DCC Preliminary Assessment
REVIEW
AGREE
MP181 next steps
AGREE
The issue
NOTE
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’

## Slide 33: What is the issue?
MAPs and meter Manufacturers wish to access smart asset-related data held by the DCC:
• Global Unique Identifier (GUID)
• Device type, Manufacturer and model
• Device firmware version
• Device status
• CSP region
• Supplier ID*
• Communications Hub make, model and firmware version**
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’
*this has been added following the request of meter Manufacturers
**this has been added following the request of the EUA

## Slide 34: What is the issue? (continued)
This data is held within the DCC Systems
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’
This data was initially thought to be confidential
Not the case if DCC is providing a service and carrying out ‘permitted business’
MP181 asks that the SEC is amended to enable DCC to provide this service as an Explicit Charge within SEC Section K

## Slide 35: Business benefit
Provide insight into the success of meter updates
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’
Access to this data will facilitate enhanced portfolio management
Allow Manufacturers to better understand the scale of the issue of out-of-date meters and firmware versions
Manufacturers will be able to provide support to Suppliers with below optimum Device / firmware versions

## Slide 36: Proposed Solution
DCC to provide a ‘paid for’ service for MAPs and Manufacturers to use
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’
DCC are to provide the dataset to the relevant MAP or Manufacturer with notification
MAPs will be requested to provide proof that they are the owner of the asset(s) via SharePoint (GUID list)
DCC are to retrieve the dataset requested by the relevant MAP or Manufacturer from the TOC
Once implemented, the service will not impact Parties not using it

## Slide 37: Preliminary Assessment key points
The requirements can be met in full and delivered using existing data available in the TOC
DCC IA to take 30 Working Days and will cost £20,000
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’
ROM costs (Design, Build and PIT): £45,000 - £65,000
Single .CSV file per MAP/Manufacturer made available on a private SharePoint or on existing DCC SharePoint on a fixed date or WD
For meter Manufacturers, extracts will be produced for all Devices relevant to the Manufacturer and will be delivered back to their own dedicated section in the existing DCC SharePoint site

## Slide 38: Costing mechanism
Explicit Charge: means the Charges calculated in accordance with Section K7, and payable in respect of the Explicit Charging Metrics.
Set up costs be will be recouped from the Explicit Charge
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’

## Slide 39: Questions for the Working Group
Can MP181 proceed to Refinement Consultation?
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’

## Slide 40: Next steps
Refinement Consultation
Change Sub-Committee
Modification Report Consultation
MP181 ‘Meter Asset Provider access to asset related data held by the DCC’

## Slide 41: Any further comments?
Bradley Baker

## Slide 42: MP155 ‘Communications Hub Re-Flash’ raised by Sasha Townsend from the DCC

## Slide 43: Objectives of the Working Group
The business requirements
REVIEW
As to whether Parties would utilise the service
PROVIDE VIEWS
MP155 ‘Communications Hub Re-Flash’

## Slide 44: Background
Communications Hubs held by SEC Parties
Installing older versions of Communications Hubs presents issues for Suppliers
The DCC believe there are more than a million Communications Hubs that are not on the most recent firmware versions being held by SEC Parties
Communications Hubs within Supply Chain
Communication Service Providers (CSPs) holding Communications Hubs ready for distribution to DCC Users may not be on the latest firmware version
Over-the-air (OTA) upgrade, when run at installation, can take a significant amount of time and increases the length of installation
SEC Parties tend to install the Communications Hubs on the latest versions first so these numbers are not reducing at speed
MP155 ‘Communications Hub Re-Flash’

## Slide 45: Issues
Current arrangements
There is no mechanism for the CSP to re-flash the Communications Hubs before delivery
Futureproofing
The return and re-flashing of Release 1.3 Comms Hubs was undertaken by CSP North in 2021
There are no provisions that accommodates a Service User returning a Communications Hub to the DCC for the purpose of re-flashing and then retaking delivery
There is not currently an Explicit Charge that could be used for this service
Modification is still required to mirror a process in CSP South and Central
Codify the liabilities associated with returning and re-flashing Communications Hubs
MP155 ‘Communications Hub Re-Flash’

## Slide 46: Business Requirements
MP155 ‘Communications Hub Re-Flash’
Ref | Business Requirement
1 | Smart Energy Code (SEC) Parties shall notify DCC when they want to re-flash Communications Hubs
2 | DCC shall notify SEC Parties whether their request for re-flashing has been accepted or rejected
3 | DCC shall confirm to SEC Parties authorisation of Communications Hub re-flash
4 | SEC Parties shall send authorised Communications Hubs to DCC
5 | DCC shall accept/reject delivery of Communications Hubs sent to DCC

## Slide 47: Business Requirements (continued)
MP155 ‘Communications Hub Re-Flash’
Ref | Business Requirement
6 | DCC shall re-flash accepted Communications Hubs
7 | DCC shall notify SEC Parties of successful Communications Hub re-flashing and re-delivery
8 | SEC Parties shall notify DCC of any amendments to re-delivery
9 | DCC shall re-deliver re-flashed Communications Hubs to SEC Parties
10 | DCC shall update the DSP inventory systems to map the new firmware version to the Communications Hub GUID

## Slide 48: Questions for the Working Group
Are the business requirements complete?
Do SEC Parties have a need for this service?
Should costs be developed on a per unit basis?
MP155 ‘Communications Hub Re-Flash’

## Slide 49: Next steps
8 Mar – Discuss business requirements with Operations Group
14 Mar – Request DCC Preliminary Assessment
4 May – Discuss Preliminary Assessment with Working Group
MP155 ‘Communications Hub Re-Flash’

## Slide 50: Any further comments?
Kev Duddy

## Slide 51: MP192 ‘Extend Scheduled Services for SMETS1 Devices’ raised by David Walsh on behalf of the DCC

## Slide 52: Objectives of the Working Group
The Impact Assessment
REVIEW
MP192 ‘Extend Scheduled Services for SMETS1 Devices’
The next steps
AGREE

## Slide 53: Summary
Background
The following SRVs cannot be scheduled:
Issue
If all Suppliers were to submit these requests On Demand, high volumes of up to around 2.7 million additional SRVs would be expected
These would likely be requested at the same time as the highest peak demand is on the DCC Total System
SRV 4.3 ‘Read Instantaneous Prepay Values’
SRV 4.4.3 ‘Retrieve Billing Calendar Triggered Billing Data Log’
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 54: What is the impact?
DSP impact
Could cause around 750 extra transactions per second
Would require two extra DSP ‘motorway lanes’ to be installed
These lanes would then go unused for the rest of the day
DSP estimate £350,000 per motorway lane, giving a total required spend of £700,000
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 55: What is the impact?
S1SP impact
The impacts would be greatest on the MOC and FOC cohorts
The increase would send both of them significantly over their contracted Transactions per Second (TPS) rates
There would be a requirement for a Dual Control Organization (DCO) uplift – very costly
The DCC estimated that figure to be £1.5million with a high tolerance and risk associated
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 56: Proposed Solution
Business Requirement
The DCC shall add DSP scheduling support for SRV 4.3 and SRV 4.4.3 for SMETS1 devices
DCC Solution
The structure of SRV 5.1 ‘Create Schedule’ will need to be changed to include SRV 4.3 and 4.4.3 – Requires XML Schema changes
The scheduling capability for SRV 4.3 and SRV 4.4.3 will be applicable only for SMETS1
If the DCC receives a request to schedule SRV 4.3 or SRV 4.4.3 for SMETS2+, the request will be rejected with a new error code introduced to notify this validation failure
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 57: Impact Assessment summary – costs
MP192 ‘Extend Scheduled Services for SMETS1 Devices’
Design | Build | PIT | Integration, SIT and UIT | TTO | Total
£63,591 | £152,908 | £175,031 | £136,726 | £25,291 | £553,907
These costs have been provided via a draft Impact Assessment and still being challenged by the DCC
The confirmed implementation costs will be provided verbally at the meeting

## Slide 58: Impact Assessment summary – impacts
Impacts
DSP and SMETS1 Service Providers
SIT and UIT will be required
SEC impacts
DUIS impacts only – XML Schema updates required
DCC note addressing just one SRV would have minimal impact on costs
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 59: Benefits and impacts
Party benefits
Suppliers will be able to schedule SRVs 4.3 and 4.4.3 for SMETS1 Devices
The DCC will receive fewer peaks in demand for these SRVs, mitigating against the need for additional capacity
Consumer
There are no perceived consumer benefits or impacts
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 60: SEC Objectives and implementation approach
SEC Objectives
Proposer believes this better facilitates SEC Objective (a):
Implementation approach
Targeting the November 2022 SEC Release
To facilitate the efficient provision, installation, and operation, as well as interoperability, of Smart Metering Systems at Energy Consumers’ premises within Great Britain
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 61: Questions for Working Group
Does the business case justify these costs?
Do you agree the modification is ready to proceed to the Change Sub-Committee?
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 62: Next steps
Change Sub-Committee review final Modification Report (15 Mar)
Modification Report Consultation (16 Mar – 6 Apr)
Change Board vote (20 Apr)
TABASC review Impact Assessment (3 Mar)
MP192 ‘Extend Scheduled Services for SMETS1 Devices’

## Slide 63: Any further comments?
Joe Hehir

## Slide 64: MP096 ‘DNO Power Outage Alerts’ raised by Del Kang on behalf of the DCC

## Slide 65: Objectives of the Working Group
The proposed changes to the legal text
NOTE
The Proposed Solution and legal text will be presented to DNOs for approval ahead of the March 2022 CSC meeting
AGREE
The update to the Proposed Solution
NOTE
MP096 ‘DNO Power Outage Alerts’

## Slide 66: What is the issue?
H3.14(g) states that Alerts must be sent to the User within 60 seconds measured from the Alert being communicated to or generated by the Communications Hub
This obligation includes Power Outage and Power Restoration Alerts
Primary impacts:
DNOs are not able to deliver the expected benefits and cost efficiencies from smart meter Power Outage Alerts and Power Restoration Alerts
The DCC is currently non-compliant for POAs and PRAs
MP096 ‘DNO Power Outage Alerts’

## Slide 67: Why is the DCC non-compliant?
Current smart infrastructure and Devices have physical technical constraints
This can only be overcome by overhauling the smart infrastructure at a significant cost
Further information found in the supporting DCC Technical Study Paper
Misalignment during the SEC’s infancy between CSP contracts and SEC obligation
System changes identified during the Development Stage offer some improvement but do not meet the requirement of 60 seconds
MP096 ‘DNO Power Outage Alerts’

## Slide 68: Refinement Consultation responses
Challenge | DCC’s response
Current performance is better than proposed targets | Separation of CSP performance targets Reduction in the proposed performance targets of 11m for POAs & 8m for PRAs Methodology for the relationship between volume of ESMEs & Performance
DNOs need further clarification about the proposed exclusions | DCC will only exclude volume where the remedy is outside of DCC’s control to improve Provide definition of proposed exemptions & justification Methodology for amending exemptions in future years
Reports have offered valuable insight & need to continue | Obligation to provide monthly reports on the POA/PRAs will be included as part of the PMR This will include details by region and break down of exclusions
MP096 ‘DNO Power Outage Alerts’

## Slide 69: Latest discussion with DNOs
The DCC’s proposed exclusions were agreed to be included at go-live and will be reviewed at the end of the first year to determine if they remain valid or should be changed or removed.
The CSP C&S 95% targets were agreed, though a second KPI may also be added to align with the CSP N.
The POA and PRA targets for CSP N need further investigation to determine a suitable measure that is meaningful to DNOs to use alongside the 95% measure. This may be the median, the upper quartile, or the point where the tail-off seen in the graphs begins. The DCC will analyse this and present proposals for agreement at a further meeting.
The proposed reporting and governance approach was agreed.
MP096 ‘DNO Power Outage Alerts’

## Slide 70: Proposed Solution
Alert delivery performance to be monitored and amended accordingly
To be split by CSP technology (while facilitating 4G CHs which will meet the SEC as written)
Amending targets (currently set at 60s) within the SEC – captured in a subsidiary document

System changes to enhance Alert delivery performance
c£10,000,000

MP096 ‘DNO Power Outage Alerts’

## Slide 71: How does this impact the legal text?
Reporting to be captured within the PMM for the PMR
Due to architecture, CSP N will have two targets at the initially proposed 95% of Alerts delivered and a to be determined value
SEC Section H will advise Parties that the target Alert delivery times are captured in a subsidiary document
MP096 ‘DNO Power Outage Alerts’

## Slide 72: Implementation approach
30 June 2022 (June 2022 SEC Release) if a decision to approve is received on or before 16 June 2022
MP096 ‘DNO Power Outage Alerts’

## Slide 73: Questions for the Working Group
Does the Working Group agree to allow DNOs to sign off the Proposed Solution and legal text ahead of the March 2022 CSC meeting?
MP096 ‘DNO Power Outage Alerts’

## Slide 74: Next steps
Agree Alert delivery targets with DNOs
Agree legal text with DNOs
March 2022 Change Sub-Committee
Modification Report Consultation
April 2022 Change Board
MP096 ‘DNO Power Outage Alerts’

## Slide 75: Any further comments?
Bradley Baker

## Slide 76: MP183 ‘Post Commissioning Obligations Reporting’ raised by Easton Brown of the DCC

## Slide 77: Objectives of the Working Group
The Proposed Solution meets the business requirements
The contents and frequency of the updated reporting suite
CONSIDER
AGREE
The draft business requirements
NOTE
MP183 ‘Post Commissioning Obligations Reporting’

## Slide 78: Overview
MP183 ‘Post Commissioning Obligations Reporting’
Background
Issue and impacts
The DCC reports on failures in Post Commissioning process for SMETS2+ Devices.
Criteria for ‘failure’ includes SRVs to update Security Credentials not being sent, or subsequent Responses not being received.
This results in failures in process pathway being conflated with failure to complete Post Commissioning.
DCC Users and CSPs waste resources investigating successfully Commissioned Devices.
Inaccurately reported volumes of Devices which fail Post Commissioning breach the Critical National Infrastructure levels for risk to the network.
Reputational damage to the industry.

## Slide 79: Draft business requirements
Ref | Requirement
1 | Devices which have not sent Responses indicating the successful execution of Commands associated with Service Requests issuing/updating Security Credentials will no longer be reported as having failed Post Commissioning.
2 | The DCC will report on the Certificate status for all Commissioned Devices throughout their lifespan.
MP183 ‘Post Commissioning Obligations Reporting’

## Slide 80: Proposed Solution – Part 1
Removal of Appendix AC ‘Inventory, Enrolment and Decommissioning Procedures’ section 5.7c.
The DCC will still report on Successful Execution of Certificate-related SRs, but this will no longer be a criteria for pass/fail of Post Commissioning.
MP183 ‘Post Commissioning Obligations Reporting’

## Slide 81: Proposed Solution – Part 2
Updated reporting suite will report on ‘in-life Certificate health’ of all Commissioned Devices.
Report will include status of all Certificate slots and count of successfully executed SRs related to updating Security Credentials.
The DCC will continue to report on the ‘seven day’ compliance with Post Commissioning Obligations.
MP183 ‘Post Commissioning Obligations Reporting’

## Slide 82: Working Group Questions
Does the Proposed Solution undermine the Post Commissioning Obligations?
Does the Proposed Solution meet the business requirements?
Are the proposed contents and frequency of the updated reporting suite suitable?
MP183 ‘Post Commissioning Obligations Reporting’

## Slide 83: Next steps
Solution Development – Mar 2022
Refinement Consultation – Apr 2022
Solution discussed with Working Group – 6 Apr 2022
MP183 ‘Post Commissioning Obligations Reporting’

## Slide 84: Any further comments? Mike Fenn

## Slide 85: AOB
Next Meeting Date: Wednesday 6 April 2022