## Slide 1: SECMP0007 ‘Firmware updates to IHDs and PPMIDs’
Raised by Npower

## Slide 2: Purpose of the meeting
The Panel has asked that we investigate the minimum viable product to reduce costs
However, the Panel does not want to cause any undue delay to the modification
We want the Working Group to advise on the feasibility of the options we have identified

## Slide 3: Agenda
Brief overview of the modification
Update on SSC discussion on local firmware updates
Discussion on options
Clarity over dual Supplier scenarios
Implementation approach
Next steps

## Slide 4: Summary
OTA firmware updates for IHDs, PPMIDs and HCALCSs via the DCC’s infrastructure
IHD/PPMID using Zigbee OTA delivery – combined distribution and activation
HCALCS using the ESME/GSME method (upgrade via modified GBCS Commands)
Solution is currently undergoing DCC Impact Assessment

## Slide 5: IHD/PPMID solution
ZigBee OTA delivery
Distribution and activation will be combined into one Service Request
Requires new GBCS use cases to distribute and return the Device firmware version
The Communications Hub is to manage the activation of firmware and the notification to the Service User

## Slide 6: HCALCS solution
ESME/GSME approach – Extension to HCALCS
Distribution and Activation are separated
Activation requires the verification against the security credentials held on the Device
HCALCS firmware activation using GBCS Critical Commands

## Slide 7: SSC discussion on local updates
IHDs and PPMIDs only

## Slide 8: Background
SSC has been looking into industry use cases to carry out triage and refurbishment of ESME and GSME
Suppliers and Manufacturers need to be able to update firmware in the supply chain
The TABASC Chair believes not allowing local firmware updates may present unnecessary constraints on Parties in the future

## Slide 9: Managing local updates
Option 2 – DSP periodically reads firmware version
DSP periodically requests firmware versions using SR11.2 and updates the inventory, perhaps once a month
Option 1 – Supplier periodically reads firmware version
Prior to carrying out any maintenance on an IHD/PPMID, Suppliers should request the current firmware version from the Device using SR11.2
The DSP will capture the response and update the SMI as a result
The firmware version usually be correct on the inventory, so might not deliver much benefit

## Slide 10: SSC recommendation
The SSC does not wish to introduce any delay to the existing approach for the modification
However, it questioned whether the Working Group has considered triage and refurbishment of IHDs and PPMIDs which would require an alternative (local) means of a firmware update
In this respect, the SSC considers that local updates are feasible subject to appropriate security controls

## Slide 11: Decision
SECAS recommend keeping the ban on local updates to prevent any further delay to the modification
  This wouldn’t prevent a Draft Proposal from being raised to reinstate local updates
The Working Group and the Proposer are asked to agree one of the following options:
  Continue to ban all local updates following the implementation of this modification
  Allow local updates to IHDs and PPMIDs only, subject to appropriate security controls
    This would require time to develop the security requirements

## Slide 12: Options

## Slide 13: Impacts
We have identified several options which may reduce the cost of this modification
We do not know how much each of these will reduce the cost by
Any changes to the assessed solution will need re-assessment by the Service Providers
  Further change requests will be required, irrespective of todays decisions
We have not been given any timescales as to how long these change requests will take

## Slide 14: Use of ESME/GSME Blocks for Updates
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
To use both memory blocks without distinction

## Slide 15: Use of ESME/GSME Blocks for Updates
Proposal
To restrict IHD/PPMID/HCALCS firmware to a single block
Why?
Use of both blocks will impact the technical architecture, but it is the testing that will drive the costs
Concerns about sleepy GSMEs – ESME updates are relatively quick, and while GSMEs can take up to 4 days, they are available the rest of the time
The number of test cases will decrease with the use of a single block

## Slide 16: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  Use of the ESME block for IHDs, PPMIDs and HCALCSs firmware
  Use of both blocks without distinction for IHDs, PPMIDs and HCALCSs firmware
Either option will require a change request

## Slide 17: Comms Hub Image SLA
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
To use a two-day SLA for Images to stay on the CH

## Slide 18: Comms Hub Image SLA
Proposal
To remove the two SLA for Images to stay on the CH
Why?
The Working Group saw no benefit in having an SLA, advising that the Image could just be overwritten
More chance of a successful update if consumer turns their Device off for long periods of time

## Slide 19: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  Remove the two day SLA for an Image to stay on the CH
    This would require a change request
  Keep the two day SLA for an Image to stay on the CH

## Slide 20: Comms Hub logging of updates
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
The CH shall record the target Device ID and the Upgrade Image File version for 15 Devices

## Slide 21: Comms Hub logging of updates
Proposal
To remove the CH requirement to log 15 Devices
Why?
The CSPs don’t currently do any such logging so this will increase costs in development and testing
The DCC note that the FW can be read from the OTA header

## Slide 22: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  Remove the requirement for the CH to log the progress of up to 15 Devices in the Upgrade Image list
    This would require a change request
  Keep the requirement for the CH to log the progress of up to 15 Devices in the Upgrade Image list

## Slide 23: Fragmented Firmware Images
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
The requirement is to fragment Images larger than 750KB

## Slide 24: Fragmented Firmware Images
Proposal
Limit firmware updates to 750KB only – remove fragmentation
Why?
Reduce costs and effort in development (less error messages, less coding, reducing expected impact on suppliers)
Fragmentation increases risks, such as Image corruption, requiring repeated image sending and overwrites – increased testing
Development is in the CHs to handle the two or more updates, not the CSPs

## Slide 25: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  To keep the requirement to fragment Images larger than 750KB
  To limit firmware updates to 750KB only – remove fragmentation
    This would require a Change Request

## Slide 26: Future Dated Update Activation
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
To allow Suppliers to future date the firmware activation

## Slide 27: Future Dated Update Activation
Proposal
Limiting the updates to immediate activation only
Why?
Significantly reduced costs in defining test cases and test execution
Increased risk as the activation date goes further into the future, with Image corruption, repeated image sending, and overwrites

## Slide 28: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  To allow for future dated activation
    Note: The SSC require that future activation be no further than 30 days in advance, in order to meet Anomaly Detection Thresholds
  To limit updates to immediate activation only
    This would require a change request

## Slide 29: Service Request for IHD/PPMID
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
To develop a new Service Request for IHD/PPMID Firmware

## Slide 30: Service Request for IHD/PPMID
Proposal
To use a new Service Request for IHD/PPMID firmware as per the original requirement
Why?
The SSC requirement for separate ADT values from ESME/GSME
The DCC have confirmed that creating SR11.4 would better this
Amending SR11.1 would likely cost more to do this

## Slide 31: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  To use existing SR11.1 ‘Distribute Firmware’ for IHDs and PPMIDs
  To use a new non-critical Service Request for IHD/PPMID firmware
    This would require a change request

## Slide 32: In-Home Displays
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
To include IHDs in the scope of the modification

## Slide 33: In-Home Displays
Proposal
Remove IHDs from the scope
Why?
IHDs have no firmware version listed in the SMI
The DSP believe 95% of all deployed displays are PPMIDs
Note that the SMETS1 programme are only including PPMIDs in their updates

## Slide 34: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  To keep IHDs in the scope of the modification
  To remove IHDs from the scope of the modification
    This would require a change request

## Slide 35: Alerts and notifications
What has been assessed?
We are still awaiting the Impact Assessment
What was the requirement?
Image Discarded
Hardware Version Mismatch
File Transfer Failure
File Transfer Success
Firmware Read Failure
Firmware Read Success

## Slide 36: Alerts and notifications
Proposal
To reduce the number of Alerts and Notifications
Why?
Suggestion that the modification should be used as a transport mechanism only
Rather than a way to deliver, monitor, and confirm the update
Would reduce development – minimal impact on testing

## Slide 37: Decision
The Working Group and the Proposer are asked to agree one of the following options:
  To keep the Alerts and Notifications referenced in the GBCS legal text
  To shorten the number of Alerts and Notifications
    Which Alerts should be removed?

## Slide 38: Forecasting firmware updates

## Slide 39: Forecasting firmware updates
The DCC have requested the Working Group provide the following information in relation to IHDs, PPMIDs and HCALCSs:
  To estimate how many Devices are deployed now
  To estimate how many Devices there will be at full deployment
  How many times they’re expected to be updated
  To estimate the number of updates expected at any one time

## Slide 40: Dual Supplier scenarios

## Slide 41: SECAS recommendation
Proposal
SECAS recommend that the Lead Supplier should only be able to carry out firmware updates in a dual Supplier scenario
Decision
The Working Group and the Proposer are asked to AGREE that the Lead Supplier should only be able to carry out firmware updates in a dual Supplier scenario
The DCC should forward the Alerts for the firmware update to the other Responsible Supplier

## Slide 42: Implementation approach

## Slide 43: Implementation approach
This modification is targeted for one of the 2021 SEC Releases
If the Impact Assessment is returned in time, and the DCC has sufficient lead time, we will aim for the June 2021 SEC Release
Note: the implementation of this modification is dependant on DCC CR1047 and CR1057

## Slide 44: Next steps

## Slide 45: Next Steps
The DCC to raise any necessary Change Requests
Service Providers to advise as soon as possible how long each Change Request will take to assess and to return a cost and timescale
SECAS will update the Modification Report with the results of this meeting
As soon as the full costs are known, we will take the Modification Report to the Panel

## Slide 46: Thank you for listening
Joe Hehir