## Slide 1: Working Group Meeting 3
25th October 2018
SECMP0031 ‘Adding UTRN functionality to SMETS’
SECMP0032 ‘Prioritising Prepayment Customers in no WAN’
SECMP0038 ‘Sending Commands via PPMIDs’

## Slide 2: SECMP0031/ Issue

## Slide 3: SECMP0031 – Update on No-WAN
The No-WAN issue has been raised with BEIS and they provided the following response. BEIS also stated that DCC were looking to identify options for providing communications for the circa 200k premises forecasted to be served by the DCC network. Findings are expected by early December:
  DCC has issued an RFI on alternative communication solutions that is seeking to identify the feasibility of using telecoms copper or other established communication technologies that do not require significant investment in infrastructure to provide smart metering communication in the following scenarios:
    Areas where coverage is not forecasted to be provided by the primary WAN technologies 2g/3g or long range radio
    “Not-spot” areas including areas of outstanding beauty and national parks
    Urban areas where cellular and radio technologies have limited penetration due to building material or other environmental factors

## Slide 4: Next Steps – SECMP0031
The Working Group are asked to consider what the next steps for SECMP0031 should be.

## Slide 5: SECMP0032 PA Review

## Slide 6: SEC Mod 0032, Description
This modification seeks to introduce a requirement on the DCC to prioritise achieving Smart Metering Wide Area Network (SM WAN) coverage in areas where:
Customers are signed up to prepayment contracts with their Suppliers
A Communications Hub (CH) is installed at a premise but does not connect to the SM WAN
The SM WAN Coverage Database indicated (at any time during the 30 days prior to the date of installation) that the SM WAN is (or would be) available in the area in which the premise is located on the installation date.

## Slide 7: SEC Mod 0032, Requirements
Business Requirement 1
The DCC will be required to achieve SM WAN coverage in 30 days (instead of 90 days) in areas where:
one or more customers within the relevant coverage area (the understanding is that these align to postcode areas) are signed up to prepayment contracts with their Supplier;
a CH is installed at a premise but it does not connect to the SM WAN;
the installation has been completed in accordance with the Communication Hub Installation Maintenance Support Materials (CHIMSM); and
the SM WAN Coverage Database indicated (at any time during the 30 days prior to the date of installation) that the SM WAN is (or would be) available in the area in which the premise is located on the installation date.
Business Requirement 2
A mechanism is to be introduced for Suppliers to inform the DCC that there is a customer signed up to a prepayment contract at a certain location. The Proposer identified that a new Service Request (SR) Self-Service Interface (SSI) would be the most appropriate solution.
Introducing a new Service Request will require corresponding changes to:
SEC Appendix AH ‘Self-Service Interface Design Specification’ sections 1.9.1, 1.9.2 and 1.10; and
SEC Appendix E ‘DCC User Interface Services Schedule'.
It is assumed that DCC will provide the corresponding redlining for the introduction of a new Service Request as part of its PA response.

## Slide 8: SEC Mod 0032, Operational Solution Option
Operational where initial analysis by the CSP might show where resolution will be needed.
In the Central and South areas (Telefonica), may provide option for CHs in surrounding homes to NO WAN to be replaced with SKU2 or SKU3 CHs, effectively raising a new mesh to remediate the problem.
For the North, the solution is to provide a new mast for a specific location. But to get a new request through Planning Regulations alone cannot be done in a 30 day lead time. Buddy Mode allows CH chaining, but requires pre-configuration, is not a true mesh solution, and not self-healing.
SM WAN incidents likely to be home specific with resolutions on a home by home basis, rather than postcode level. Can possibly identify problem areas (postcodes) where coverage will be a problem, but hard to confine it to a specific area around an anticipated PPMID.
If Energy Supplier does not own supplies to homes requiring new CHs, that Energy Supplier cannot resolve the incident on their own. Energy Suppliers would be required to coordinate a common installation time for the correct, new CHs to be installed but the other Energy Suppliers have no obligation to do so. In Centre and South, could be overcome by TEF accompanying the Energy Supplier for all visits, but will increase costs in the charging model, and a significant increase in T3 installs.
Geographic variations with risk that 30 day timeline is not feasible. This approach would raise the cost to the Service Users significantly with the risk of over-specifying the features for an installation.
Notes: Note there is no DSP data on PPMIDs before an install, and can be changed without updating DSP

## Slide 9: SEC Mod 0032, Meter Data Analysis Option
Alternative option combines data to predict potential No WAN:
CSP Data, indicating how installs were carried out
Utility and Energy Supplier Data, where cases of Prepayment Meters are already known, or in place
DCC data, where existing Registration Data from an earlier smart meter installation is available; this data includes Customer Type
If installation data could be shared, it should be possible to analyse existing data for failed and successful installations, to predict coverage and signal strength. DCC would be responsible for aggregating the data, providing the data analysis, and making this information available to energy suppliers prior to an installation. Energy suppliers then responsible for providing the required resources for an installation.
Coverage Checker -- postcode-based in the Northern area, and premise-based in the Central and Southern. Includes coverage and CH info, but not customer or meter type (Credit / PPM?). Would require reconfiguration of the Self Service Interface and Coverage Checker.
This work to establish the data required for the analysis and the sharing of information prior to an installation is likely to be significant and lengthy to implement. Similar SEC Mods costed at between £1 and £2 million (although this looks very optimistic).
Notes: Note: Prepayment Meter info is considered personal information under the General Data Protection Regulation, would require additional data processing and security implementations to keep data secure.

## Slide 10: SEC Mod 0032, Major Concerns
Prepayment - The SECMP applies only for PPM consumers.
Statistically likely at least 1 PPM per postcode in the UK - solution needs to cover the whole of the UK
DCC Total System cannot detect where PPM energy consumers are, SPs cannot discriminate them
90 days  30 days
even if possible there will be massive impact on current processes
Changes will have substantial regulatory, contractual, process and cost impacts.
Changes will require commercial negotiation, SPs indicated considerations in the region of £500m each.
Other
Significant additional obligations need to be placed on the Energy Suppliers to guarantee resolution.
Prioritising one consumer group over another is not catered for in the SEC. CSPs see their estate as one and are unaware of who is responsible for CH. Cannot prioritize one Energy Supplier’s customers over another set as this would be anti-competitive.
Note: For SMETS2, PPM designed to operate in the absence of SM WAN as long as:
Devices are paired locally in the premises
A PPM with a local payment option is used
The consumer is appropriately informed and educated, which they must be under the SMICoP code
This should cover most cases, such that SMETS 2 meters should not be subject to these considerations.
Notes: No hard and fast information regarding the distribution of Prepayment meters across postcodes. There are about 1.8 million postcodes, 4.5 million electricity prepay and 3.5 million gas prepay meters, which infers an average of between 2 and 3 electricity prepayment meters and 2 gas prepayment meters per postcode.
We have requested further information on the distribution of Prepayment meters from the Working Group. If there is at least one Prepayment Meter per postcode, then the Requirements of the SEC Modification may not be valid and the business benefit very limited.

## Slide 11: SEC Mod 0032, Recommendation
Operational-based change would face significant logistical obstacles and would require large changes to the existing process, with no guarantee that a 30 day deadline could be met.
Timelines suggest technical delivery in June 2020, with reduced business benefit.
Based on the associated technical difficulties, the low business benefit, and anticipated extremely high costs of delivering a solution, the recommendation is that this SEC Mod is not progressed on the Operational Basis.
A Meter Data Based option could be considered using meter type and surrounding historical install data prior to an installation is feasible, but work to establish the data availability and sharing of information is likely to be difficult and costly.
Notes: In addition, in October we will be proceeding with a RFI seeking to identify the feasibility of using telecoms copper or other established communications technologies that do not require significant investment in infrastructure to provide smart metering communications in the following scenarios:
Areas where coverage is not forecasted to be provided by the primary WAN technologies 2g/3g or long range radio
“Not-spot” areas including areas of outstanding beauty and national parks
Urban areas where cellular and radio technologies have limited penetration due to building materials or other environmental factors

## Slide 12: SEC Mod 0032 and 38 Definitions
“No WAN”, a situation where it is not possible for devices and the CH to communicate over the WAN. Applies where the Coverage Checker indicates coverage but in reality a WAN connection is not possible. SECMP0038 does not include the No-WAN scenario.
“Intermittent WAN”, a situation where it was possible to commission devices over the WAN, but subsequent communication between devices and the DCC Total System over WAN fails. This could be caused by changes to the building or surroundings of the premises adversely affecting the WAN communications. SECMP0038 focusses on just the intermittent WAN case.
Notes: was defined by the Working Group as
The Working Group suggested that missing WAN communication for a time period between one and three weeks should be considered an Intermittent WAN situation.

## Slide 13: SECMP0032 – Proposed Legal Text (1)

## Slide 14: SECMP0032 – Proposed Legal Text (2)

## Slide 15: SECMP0032 – Proposed Legal Text (3)

## Slide 16: Next Steps – SECMP0032
  The Working Group are asked to consider how they wish to proceed with the Working Group Consultation after reviewing the legal text and Preliminary Assessment.
  The Working Group are asked to consider whether they should move forward with the proposed alternative solution and develop the solution design specifications.

## Slide 17: SECMP0038
Proposed Solution
Risk Assessment Requirements

## Slide 18: SSC views on SECMP0038
On the 10th October SECAS presented the proposed solutions for SECMP0038 to the SSC. The SSC advised carrying out an external Risk Assessment to determine the risks and impacts.
Extract of the minutes below:
“The SSC need to understand the technical solution and this needs to be risk assessed along with the controls that will be put in place. The SSC considered that the scale of the security implications requires a security risk assessment to be conducted by a Competent Independent Organisation (CIO) procured via the WG and for the scope of the risk assessment and the outcome to be agreed by the SSC. The SSC also noted that there needs to be a clear business case based on SMETS2 service levels. The SSC advised that the WG / Change Team should bring in an external CIO in order to perform the security risk assessment with the scope and outcome agreed by the SSC”.

## Slide 19: Risk Assessment
The Working Group are asked to confirm:
  The SSC rationale for needing a Risk Assessment for SECMP0038 proposed solution
  The need for a request to the SEC Panel for a Risk Assessment to be commissioned (next Panel meeting is on the 9th November)
  The feasibility of an external company being able to carry out the Risk Assessment based on the requirements presented following this Working Group, rather than an internal or DCC-led Risk Assessment

## Slide 20: Standard Communication Smart Meter System
Authentication
& Encryption
Secured
Transmission
Protected LAN
CH
ESME
GSME
SM WAN
DSP
Internet
DCC
User
PPMID
SM HAN

## Slide 21: Communication via PPMID
CH
ESME
GSME
SM WAN
DSP
Internet
DCC
User
PPMID
SM HAN
Internet
Firewall & Protection
against attacks,
DoS, replays etc
need defining

## Slide 22: Next Steps – SECMP0038
  The Working Group are asked to consider whether they wish to go forward with commissioning a Risk Assessment, either with an external party, internal or DCC, as per the advice of the SSC.

## Slide 23: Annex

## Slide 24: General SEC Objectives
(a) facilitate the efficient provision, installation, and operation, as well as interoperability, of Smart Metering Systems at Energy Consumers’ premises within Great Britain;
(b) enable the DCC to comply at all times with the General Objectives of the DCC (as defined in the DCC Licence), and to efficiently discharge the other obligations imposed upon it by the DCC Licence;
(c) facilitate Energy Consumers’ management of their use of electricity and gas through the provision to them of appropriate information by means of Smart Metering Systems;
(d) facilitate effective competition between persons engaged in, or in Commercial Activities connected with, the Supply of Energy;

## Slide 25: General SEC Objectives
(e) facilitate such innovation in the design and operation of Energy Networks (as defined in the DCC Licence) as will best contribute to the delivery of a secure and sustainable Supply of Energy;
(f) ensure the protection of Data and the security of Data and Systems in the operation of this Code;
(g) facilitate the efficient and transparent administration and implementation of this Code; and
(h) facilitate the establishment and operation of the Alt HAN Arrangements.