## Slide 1: Joint SEC / DCUSA Working Group SECMP0046 ‘Allow DNOs to control Electric Vehicle chargers connected to Smart Meter infrastructure’ DCP 371 ‘Last resort arrangements for Distributors to manage specific consumer connected devices’

## Slide 2: Joint Working Group
Outcomes
Understand why the SEC technical solution was selected
Understand what the DCUSA governance is required
Agree some minor amendments
Outcomes

## Slide 3: Solutions discussed previously
Smart EV charger/Load
HCALCS connected EV charger/Load
Supplier Management of Whole-Meter Load
Contract with Ancillary Services Provider
Pulse Width Modulation
Use of Type 2 Devices

## Slide 4: HCALCS to be used as a last resort
Tools available to prevent feeders overloading
• Time of Use (ToU) tariffs
• Vehicle to Grid (V2G) as Ancillary Services
• Supplier sets load limit for whole meter through Suppliers control load
• Use of other Ancillary Services
The Proposed Solution for SECMP0046 is to be used as a last resort

## Slide 5: Solution 1: Smart EV charger/Load
Proposed Solution
Use the DCC Systems to pass signals to HAN-connected smart charger/Load
Vary the rate of charging/Load in response to a parameter passed to it
Not Progressed
EV charger/Load would have to be CPA approved – costly
Prevent innovation of EV chargers/Load controllers

## Slide 6: Solution 2: HCALCS connected EV charger/Load
Proposed Solution
HAN connected Auxiliary Load Control Switch
HCALCS to decrease domestic EV charger/Load electricity supply
Electricity Distributor to have permission to send signals when overload event is detected
Progressed
This Proposed Solution has been selected for progression

## Slide 7: Solution 3: Supplier Management of Whole-Meter Load
Proposed Solution
In the case of an overloading event the Distributor would inform the relevant Supplier
Supplier would send SRV 6.4.1 to cap load on ESME*
Not Progressed
The timeframe is too short to identify and contact the correct Supplier
In the case of a feeder failure the response time needs to be approximately 30 seconds**
*This solution requires the Supplier controlling the load using the DCC Service Requests, not via flexibility
**The 30 seconds refers to one of three DCC SLA response times (30 seconds, 5600 seconds or 24 hours)

## Slide 8: Solution 4: Electricity Distributor contract with Ancillary Services Provider
Proposed Solution
Contract between ASP and Electricity Distributor
ASP to manage load locally to stabilise load on LV network
Not Progressed
ASP may not be available on a particular feeder
It is expected that DNOs will make an attempt to secure flexibility before using the solution to this modification
The solution of this modification is to be the last resort after all other options have failed

## Slide 9: Solution 5: Pulse Width Modulation
Proposed Solution
PWM to allow modification of EV charger/Load if an overloading event is detected
Not Progressed
A new SMETS Device would have to be developed
Dismissed to similarities with initial proposed solution of a Smart EV charger/Load controller

## Slide 10: Solution 6: Use of Type 2 Devices
Proposed Solution
Use of CADs / Type 2 Devices
Simple to implement
One-way signal to domestic EV charger/Load
Not Progressed
Cannot receive external signal and will only alter load based on predefined parameters

## Slide 11: BEIS Developments
OLEV/BEIS have been running a trial to develop an APC/SAPC
BEIS will be designating this functionality into the SEC in November 2020

## Slide 12: How do we get to last resort?
Load on feeders and substations automatically monitored-if load reaches a predetermined level (90%) then flexibility services tender issued
If load begins to increase flexibility contract renegotiated
Network Outage Occurs
New provider appointed. If no interest in providing services or cost uneconomic then last resort solution implemented
Customers with EV Charging equipment contacted and asked if they wish to participate in the last resort solution to mitigate network interruptions while a permanent solution is investigated and put in place
Last resort solution implemented for a maximum of 12 months
DNO investigates permanent solution to the situation. Options include upgrading cable, overlaying cable, replacing transformer, new smart solutions as they become available. Further flexibility tender

## Slide 13: Any questions about the solution?

## Slide 14: Business Requirements update
The customer will be able to receive a notification to their IHD when their Electric Vehicle charging is curtailed
Electricity Distributors will be alerted when a Supplier attempts to unjoin necessary Devices connected to the Electric Vehicle
To be consolidated through SECMP0062 solution?

## Slide 15: Other Code Changes

## Slide 16: BSC Settlement Issues
This has been raised in the SEC Working Group and DCUSA Working Group
Where an EV is curtailed the Supplier would be out of Balance and incur penalties

## Slide 17: Maximum energy deferred

## Slide 18: BSC Conclusion
SEC and DCUSA are working closely with the BSC to manage any cross code changes
The BSC have said no changes are needed prior to SECMP0046 implementation

## Slide 19: BSC Rationale
Consumer impact and volumes are relatively small
Issue 89 is looking at wider BSC changes in light of DNOs using flexibility. Any impact should be considered under the wider reaching DNO flexibility project
The BSC recommend future solutions to DNO flexibility should not be constrained by any modification raised now to address the issues in SECMP0046

## Slide 20: Governance questions

## Slide 21: What has been asked of the DCUSA Group?
what does ‘Last Resort’ mean?
Who is responsible for any metering/charging equipment/ heat pump faults post a DNO intervention?
GC147 may provide some guidance on compensation
Possible answer by 25 October 2020

## Slide 22: Clean Energy Package
A new licence condition (31E) on the Procurement and Use of Distribution Flexibility Services. This condition requires us to procure and use distribution flexibility services where it is economic and efficient to do so and in accordance with objective, transparent and market-based procedures
Ensure that this is fair (non-discriminatory) and open to all potential market participants and it requires us to exchange all necessary information with the GBSO to achieve optimal utilisation of resources

## Slide 23: Cost Benefit Analysts/Business Case
Base cost for speed of uptake based on 10% of overloaded networks
Base cost for market failure based on 7% failure rate
£2,467,480
£11,511,449

## Slide 24: Next Steps
DCC Impact Assessment
Proposed Implementation date
DCP 371 Consultation
DCUSA Impact Assessment

## Slide 25: SEC Modification name change
‘Allow DNOs to control Electric Vehicle chargers connected to Smart Meter infrastructure’
SECMP0046
‘Allow DNOs to control load connected to Smart Meter infrastructure’