## Slide 1: Comms Hubs & Networks Programme: Design Update for TABASC
We believe in making Britain more connected, so we can all lead smarter, greener lives.
TABASC 90_0106

## Slide 2: The Ask
DCC Comms Hubs and Networks Programme
To provide TABASC with an update on:
  CH&N General Design [TABASC57X/CONF02]
  4G Comms Hub Compatibility with Existing SMETS2 Devices and Meters
  4G Coverage Information Provision [TABASC68X/CONF04 & TABASC68X/CONF05]
For Discussion

## Slide 3: Topic 1: CH&N General Design

## Slide 4: CH&N General Design
Content of these Slides
These slides provide a general update on the CH&N design, aiming to address TABASC57X/CONF02
Topic Context
DCC has committed to share key design information with TABASC, and in particular liaise on key design decisions
DCC has now worked through the low level designs and so can share advanced designs
Action Ref | Action
TABASC57X/CONF02 | DCC to return to the TABASC to seek agreement on the design options following the conclusion of the RFP.

## Slide 5: CH&N General Design
Design Objective
The CH&N programme is a strategic uplift in capabilities that focuses on the future of DCC operations in the Smart Metering environment by designing and procuring future-proof Communication Hubs and Network services. The CH&N programme will deliver new 4G Communication Hubs and the supporting infrastructure to ensure that the minimum 15-year operational asset life from the point of installation is realised. The core objective of this initiative is to address the impact of 2G/3G technology obsolescence.
Design Components
Components including Communications Hubs, a compatible wide area network and a compatible device manager solution will be introduced. Necessary augmentations to the Data Services Provider (DSP) will be implemented. CH&N is designed such that the DCC Service Users systems and SMETS2 smart metering devices will not need any adaptations to communicate with one another over CH&N
Major Design Changes
No major changes have been made to the CH&N design during the low level design (Design Phase 3) that has occurred since procurement and contract signature, and since previous TABASC liaison

## Slide 6: CH&N General Design
Communication Hub
ZigBee HAN 2.4GHz/Sub-GHz SEP 1.4
GBCS 4.1
eUICC (e-sim)
LTE CAT1 700/800MH bands
Wide Area Network
3GPP compliant
99.25% coverage
IPV6 CH addressing
Coverage checker
Cloud for bespoke part
Device Manager
Microservices architecture
Cloud hosted application

## Slide 7: CH&N General Design
Decision # | Design Phase | Title | Design Decision | Rationale
DBT-D-001 | 3 | Coverage Information Provision / Coverage Checker | Option A [same query / response includes 2G/3G and 4G datasets] will be developed at risk | Based on preliminary Service User feedback, this is the most technically efficient way to obtain coverage information (TABASC and SEC Ops Groups were consulted) No change to the way in which Service User queries are submitted Service Users receive full insight into coverage information
DBT-D-010 | 3 | Management of WAN Gateway IP Address Stored Within the CHs | Management of WAN Gateway IP addresses within the CHs will remain as is and will be managed within the firmware. | This is the security-approved, proven current way of working Capability for the Device Manager to remotely change the WAN GW IP address stored within the CH can be developed as a roadmap item if required
DBT-D-012 | 3 | Power Restoral Alerts Provision to Service Users | Power Restore Alerts (PRAs) will not be sent from the Device Manager to the Data Service Provider. | This is the current way of working Based on DNO feedback, there is still no requirement foreseen for PRAs to be sent to Service Users
DBT-D-015 | 3 | Nomenclature for 4G Comms Hub | For the 4G Comms Hub, it is proposed: Comms Hub Variant = ‘4G Cellular DB’. Its associated WAN Variant = ‘4G Cellular’. This is an addition to the nomenclature used in SEC | The 4G Comms Hub needs to be distinguished from the 2G/3G Comms Hub in the DSP, Comms Hub Manufacturer and DCC data models Prefixing 4G provides a clear and simple means of distinguishing
DBT-D-036 | 3 | Power Outage Alerts Retry Mechanism | The retry time for sending of Power Outage Alerts from the Device Manager to the DSP shall be a maximum 24 hours (the process is also known as buffering) | DNOs have expressed an aspiration to receive all Power Outage Alerts that occur during a DCC system outage (planned or unplanned) A finite timescale for buffering needs to be stipulated to make the requirement testable
DBT-D-047 | 3 | Anomaly Detection Within Comms Hubs | Requirements deferred for anomaly detection within Comms Hubs | DCC need time to get the requirements right. There is a risk that if DCC get the requirements wrong there could be negative consequences to performance of the Comms Hubs. This will be included as part of the Comms Hub roadmap.
DBT-D-051 | 3 | Alert Storm Protection Within Comms Hubs | Requirements deferred for alert storm protection within Comms Hubs | Defer requirements to a later release as changes could have GBCS / SEC change implications. 4G Comms Hub is no worse than 2G/3G solution that also does not include this capability.
Design Decisions of Relevance to TABASC – Design Phase 3

## Slide 8: Topic 2: 4G Comms Hub Compatibility with Existing SMETS2 Devices and Meters

## Slide 9: 4G Comms Hub Compatibility with Existing SMETS2 Devices and Meters
Content of these Slides
These slides demonstrate how the 4G Comms Hub is indeed compatible with existing SMETS2 devices and meters in an economic and efficient manner
These slides detail how this compatibility is achieved through design and build and assured through testing
Topic Context
Within the CH&N Dual Band Final Business Case (FBC), DCC stated that “The Communications Hub is fully compatible with existing SMETS2 devices and meters, allowing Energy Suppliers to swap out the Communications Hub while leaving other elements of the installation in place” (page 33)
In the letter produced by BEIS / The Department regarding non-objection to the CH&N Dual Band FBC, it was stated that “It will be important for DCC to demonstrate to industry, via the SEC Panel, the detail of how these outcomes will be achieved in an economic and efficient manner” (annex E; paragraph 3)

## Slide 10: 4G Comms Hub Compatibility with Existing SMETS2 Devices and Meters
Design and Build to Achieve Compatibility
In order to achieve compatibility with existing SMETS2 devices and meters, the 4G Comms Hub is designed and built according to the relevant standards and specifications, including:
the Communications Hub Technical Specification (as defined in the Smart Energy Code)
the GB Companion Specification (version 4.1)
the Intimate Communications Hub Interface Specification (ICHIS)
Specific Components to Achieve Compatibility
In order to interface with existing SMETS2 devices and meters, the 4G Comms Hub includes a dual-band HAN module that can interwork using ZigBee with the existing HAN modules present within existing SMETS2 devices and meters

## Slide 11: 4G Comms Hub Compatibility with Existing SMETS2 Devices and Meters
HAN Module Overview & Rationale for Design
HAN Module
ZigBee R22, Memory 256kB/1.536MB)
WAN RF System
(700 MHz and 800 MHz)
WAN Module
(LTE Cat 1, Memory 256MB/512 MB)
Power Supply Management
Meter Interface
HAN RF System (EFR32MG24 - 2.4GHz and 868 MHz- Si4468)
eUICC
Security Module (IC Vault)
SMHAN functionality provided by latest SiLabs Chipset EFR32MG24 and Stack Version 7.x (with ZigBee Certified Stack)
EFR32MG1 not recommended by SiLabs for new design due to limitations in memory and ZigBee Stack upgrades to future versions
Aspect | 2G/3G CH | 4G CH | Impact of change
Chipset | EFR32MG1 | EFR32MG24 | Both chips from same family New chip from SiLabs and require stack version > 7.x series
RF (2.4 GHz and 868 MHz) | EFR32MG1 (2.4Ghz) RF Chip - Si4468 (868 MHz) | EFR32MG24 (2.4Ghz) RF Chip - Si4468 (868 MHz) | Improvement expected on 2.4GHz receive sensitivity (~5.5dB)
SiLabs Stack Version | 6.7.10 | 7.x | Improved security Improved features with bug fixes
Processor on Chip | ARM Cortex M4 | ARM Cortex M33 | New Chip 20% more performance.
Memory | RAM – 32kB, Flash – 256kB | RAM – 256 kB, Flash – 1.5MB | Future proof stack and application upgrades with 15 years lifetime
Comparison between 2G/3G CH and 4G CH GBCS 4.1 compliant – SMHAN (H/W and S/W)

## Slide 12: 4G Comms Hub Compatibility with Existing SMETS2 Devices and Meters
Assurance of Compatibility
The functional interoperability of the 4G Comms with other HAN Devices is validated in Comms Hub PIT
There are two key areas which help to achieve this:
  The use of an approved list of Device Models from each Device Type, as output by the Device Selection Methodology (full list available on next slide).
  The running of Test Scope appropriate to validate the interaction between the 4G Comms Hub and the full list of In Scope Device Models.
    As examples, this will cover items such as Whitelisting and joining Devices, GPF Mirroring, provision of operational data from the GPF, handling network key changes, TCSO etc..
These items are captured in detail in the CH&N Test Coverage Document and its appended Coverage Traceability Document, which has been agreed with TAG (in Feb 2023 via TAG98_X).

## Slide 13: 4G Comms Hub Compatibility with Existing SMETS2 Devices and Meters
Device Type | HAN | Manufacturer | HW Variant | Firmware | GBCS Version | Inclusion Reason
ESME | 2.4 GHz | 1063 (L&G) | 00050204 | 38040404 | 3.2 | Manufacturer Coverage
ESME | 2.4 GHz | 106C (EDMI) | 10E2A100 | 0314B700 | 3.2 | Manufacturer Coverage
ESME | 2.4 GHz | 118F (Aclara) | 00000107 | 0007080A | 3.2 | Manufacturer Coverage
ESME | 2.4 GHz | 1057 (Honeywell) | 00000101 | 09014007 | 3.2 | Manufacturer Coverage
ESME | 2.4 GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
GSME | 2.4 GHz | 1063 (L&G) | 47720101 | 03033254 | 3.2 | Manufacturer Coverage
GSME | Sub GHz | 1063 (L&G) | 47820101 | 15015131 | 3.2 | Manufacturer Coverage
GSME | 2.4 GHz | 106C (EDMI) | 10F2A100 | 0309B700 | 3.2 | Manufacturer Coverage
GSME | Sub GHz | 106C (EDMI) | 10F3A100 | 0389B800 | 3.2 | Manufacturer Coverage
GSME | 2.4 GHz | 1057 (Honeywell) | 05750101 | 00020C0C | 3.2 | Manufacturer Coverage
GSME | 2.4 GHz | 1015 (Flonidan) | 09B33700 | 13030A0A | 3.2 | Manufacturer Coverage
GSME | Sub GHz | 123E (Flonidan) | 00010600 | 01060605 | 3.2 | Manufacturer Coverage
GSME | 2.4 GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
GSME | Sub GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
PPMID | 2.4 GHz | 10E0 (Chameleon) | 000F0001 | 00010000 | 3.2 | Manufacturer Coverage
PPMID | 2.4 GHz | 10E0 (Chameleon) | 00051200 | 00080201 | 1.1 | GBCS Version Coverage
PPMID | 2.4 GHz | 10E0 (Chameleon) | 000B0100 | 00010300 | 2.1 | GBCS Version Coverage
PPMID | Sub GHz | 10E0 (Chameleon) | 000D0001 | 00010100 | 3.2 | Manufacturer Coverage
PPMID | 2.4 GHz | 1090 (Geo) | 00080100 | 05070100 | 3.2 | Manufacturer Coverage
PPMID | Sub GHz | 1090 (Geo) | 00070200 | 05100000 | 3.2 | Manufacturer Coverage
PPMID | 2.4 GHz | 1128 (IHDL) | 00050101 | 02010100 | 3.2 | Manufacturer Coverage
PPMID | Sub GHz | 1128 (IHDL) | 00060101 | 01240000 | 3.2 | Manufacturer Coverage
PPMID | 2.4 GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
PPMID | Sub GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
HCALCS | Sub GHz | 119A (SLS) | 0001022B | 01000010 | 3.2 | Manufacturer Coverage
HCALCS | 2.4 GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
HCALCS | Sub GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
SAPC | 2.4 GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
SAPC | Sub GHz | 119A (SLS) | Emulator | Emulator | 4.1 | GBCS Version Coverage
The table to the left shows the Device Models approved for inclusion in CH PIT testing.
These are based on the outputs of the CH&N Device Selection Methodology as approved for inclusion in the CH&N Test Approach Document.
Agreed through TAG.
In Scope Devices – Comms Hub PIT

## Slide 14: Topic 3: 4G Coverage Information Provision

## Slide 15: 4G Coverage Information Provision
Content of these Slides
These slides provide an update on DCC’s intent regarding provision of 4G coverage information plus address:
  TABASC68X/CONF04 “The DCC to spend more time developing business process scenarios in relation to the use of the proposed WAN coverage database”
  TABASC68X/CONF05 “The DCC to arrange a dedicated workshop open to interested members of the TABASC and OPSG to collect feedback on coverage look-up arrangements”
Topic Context
According to the Smart Energy Code (SEC), each Wide Area Network (WAN) Service Provider must compile and maintain a coverage database for their geographic service area
According to the SEC, prior to each new install, Service Users must query the coverage database to check that there is coverage at the intended premises and to see which Comms Hub variant should be used (as well as Auxiliary Equipment, if applicable)
At present, the smart metering communications infrastructure in GB is divided into three Regions – North, Central and South, with each Region covered by a single, unique WAN Service
With this arrangement in place, the coverage lookup service that must be used prior to a new installation returns one WAN Service Provider per premises with one specific Comms Hub Variant to use
However with the introduction of 4G, at least one additional WAN Service Provider / Comms Hub Variant will be added to the arrangement in the Central and South Regions
This raises the question: how should coverage information be provided given multiple Service Providers per Region?

## Slide 16: 4G Coverage Information Provision
DCC’s Proposal for Coverage Information Provision
From the point of 4G service go-live in the Central and South Regions, there will be potential to perform new installations using either the existing 2G/3G service (with a 2G/3G CH) or using the new 4G service (with a 4G CH)
  Service Users can choose to install using either 2G/3G or 4G during this period, which allows for both a transitional window and/or for any residual stocks of 2G/3G CH to be used up
  Coverage information for both 2G/3G and 4G will need to be made available to Service Users in order to support this
  DCC’s proposal is that coverage requests submitted via DUIS or SSI will have coverage information for both 2G/3G and 4G. The rationale for this view, based on preliminary Service User feedback, is that this is the most technically efficient way to obtain coverage information. The alternative would be that Service Users should specify for which service coverage information is sought as part of their coverage request
One exceptional scenario where the 2G/3G service must be used, even if 4G is available, is when the 2G/3G coverage information indicates that the Comms Hub will act as a 'Mesh Gateway’
  Failure to install a Mesh Gateway where required could jeopardise the ability to connect dependent Comms Hubs (termed 'Mesh Nodes’).

## Slide 17: 4G Coverage Information Provision
Update on TABASC Action Ref TABASC68X/CONF04
Current Thinking
As the CH&N procurement and design has progressed, the situation faced has become far simpler
  There will be only one 4G WAN Service Provider; so in actuality there will be no complex need to somehow decide between different 4G WAN Service Providers
  2G/3G coverage information will have to be reviewed by Service Users for each intended install as well as 4G coverage information, due to the need to consider if a ‘Mesh Gateway’ is specified for the premises
Thus in actuality there is only one, relatively straightforward business scenario: to provide 2G/3G coverage information as well as 4G coverage information prior to each install
Action Ref | Action
TABASC68X/ CONF04 | The DCC to spend more time developing business process scenarios in relation to the use of the proposed WAN coverage database.

## Slide 18: 4G Coverage Information Provision
Update on TABASC Action Ref TABASC68X/CONF05
Current Thinking
As the CH&N procurement and design has progressed, the situation faced has become far simpler
Solution options for the arrangement have been discussed on several occasions with TABASC, OPSG and during a dedicated slot at a transition workshop in Feb 2023
Consistently the consensus feedback has been that the arrangement should be: Service User submits a coverage request as per the as-is query; the resultant response contains coverage information for 2G/3G and for 4G
This arrangement will be reflected in a future version of DUIS (5.3)
Action Ref | Action
TABASC68X/ CONF05 | The DCC to arrange a dedicated workshop open to interested members of the TABASC and OPSG to collect feedback on coverage look-up arrangements.

## Slide 19: Any Questions?