## Slide 1: SEC Change Ad hoc Working Group meeting SECMP0062 and SECMP0067 – November 2019

## Slide 2: DCC Traffic Management Overview

## Slide 3: Traffic Management
DCC Update

## Slide 4: Traffic Management Device Alerts
ISFT daily alert volumes were projected to be 2 million. As of November 14th 2019, daily alert volumes were 34 million with less than 10% of smart meters installed
8F3E alerts are generated by (< 0.1%) commissioned devices but account for 80% of device alerts. A single meter can generate 60,000 alerts in a day
SMETS1 meters are triggering device alerts at comparable rates to SMETS2

## Slide 5: Traffic Management SRV’s
ISFT 5 daily SRV volumes projected to reach 250 million. Daily SRV volumes today are below 5 million
SRV daily volumes naturally fluctuate over the day. Anomalies may lead to concentrated traffic bursts

## Slide 6: Traffic Management The Problem
High volumes of SRV’s and device alerts have two potential impacts on the DSP:
Processing alerts or SRV’s: The current capacity for processing device alerts is 130m per day and SRV’s 40m. Above these thresholds there will be a deterioration in performance which will result in device alerts or SRV’s being rejected indiscriminately
Storing device alerts: In the event device alerts cannot be delivered to service users, they are stored in memory. At current volume, the storage capacity for all service user alerts is 5 hours. For the Service User receiving the most alerts, it is 32 hours
High volumes of SRV’s and device alerts impacts on Service Users:
Processing of alerts and SRV’s: Service Users are currently experiencing issues processing current device alert volumes while their systems are operating. If a service user experience a system outage this problem is exacerbated by the backlog of device alerts stored at the DSP

## Slide 7: Traffic Management Actions
TOC are monitoring, investigating and reporting on the number of problem device alerts
  TOC share Top Talker reports with service users
  TOC identifies which devices need their firmware updated
  TOC investigating root cause of Top Talkers
DCC capacity management regularly reviews system and component utilisation and performance to ensure that service capacity matches service user requirements
DCC analyses system traffic for early indicators of erratic behaviour
DCC is working with service users to undertake all reasonable steps to reduce device alerts
CSP’s are working to identify solutions at the device level
  For example, throttling or consolidation of alerts could be implemented on the HAN device
  DCC to work with service users to understand their processing capabilities and establish a throttling mechanism to align traffic volumes with their system capabilities

## Slide 8: Check Point
Does this resolve the Change Board Issues?
Is any further work needed on this issue?
Moving Forward with SECMP0062 and SECMP0067
Has this information allowed us to understand why SECMP0062 and SECMP0067 need to be progressed?
Does the Working Group agree that SECMP0062 and SECMP0067 should be progressed independently?
Are there any outstanding issues that need to be addressed?

## Slide 9: Any Questions

## Slide 10: SECMP0062

## Slide 11: DCC answers to the issues raised on SECMP0062

## Slide 12: Any Questions

## Slide 13: Next Steps

## Slide 14: Next Steps and Timelines
December Panel*
January Change Board vote
Modification Report Consultation
* Assuming all questions have been answered satisfactorily

## Slide 15: SECMP0067

## Slide 16: DCC answers to the issues raised on SECMP0067

## Slide 17: Any Questions

## Slide 18: Next Steps

## Slide 19: Next Steps and Timelines
Refinement Consultation*
Modification Report Consultation
January Panel
IA request
* Assuming all questions have been answered satisfactorily

## Slide 20: Any Outstanding Issues

## Slide 21: Thank you for attending